## Slide 1: CNT4007C: Theory and Fundamentals of Computer Networks
Course Overview
Dr. Ezhil Kalaimannan
Content derived from various sources including Tomsho et al., Guide to Networking Essentials,
Kurose and Ross, Computer Networking: A Top-Down Approach

## Slide 2: Overview of Computer Networks
Definition and benefits of networking.
Network types and structures.
Network protocols.
  OSI Reference Model
Network applications.

## Slide 3: What is a Computer Network?
Definition: A collection of computers and devices that are physically connected to each other via a wired or wireless medium.
Network components:
  Routers, hubs, and switches for distributing data packages.
  Network cards for connecting computers and devices to networks.
  Twisted pair network cables, coax cables, fiber-optic cables, …
Network sizes may vary from home networks to the Internet.
  Home network may include 2 computers and a printer.
  Internet includes millions of computers and other network devices.

## Slide 4: Motivation for Building Computer Networks
Resource distribution and sharing
  files and devices such as printers or scanners may be shared
  personal files can be accessed from remote locations
Communication between hosts
  message passing between hosts supporting information exchange and services (e.g. email, e-learning, Web, etc.)
Distributed computing
  computers in network may solve a computing problem jointly (e.g. Seti@home, …)
Improved reliability
  replication of data across a network aids in securing data access should individual hosts storing the data fail

## Slide 5: Network Types
Local-Area Network (LAN)
  Usually covers one building (sometimes a few nearby buildings)
  Links multiple computers and devices
  Can be very fast (e.g. Gigabit Ethernet)
Metropolitan-Area Network (MAN)
  Usually covers the area of a city or a small geographical region
  Links multiple LANs within a geographical region
  Speed varies between 30 to 150 Mbits/sec.
Wide-Area Network (WAN)
  Usually spans large geographical area such as country.
  Connects multiple MANS within a large region using high-bandwidth links
  Speed varies greatly depending on network traffic and underlying technology that implements the network.
  Internet is the largest WAN spanning the entire globe.

## Slide 6: What’s the Internet: “nuts and bolts” view
millions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
Notes: 6

## Slide 7: What’s the Internet: a service view
Infrastructure that provides services to applications:
  Web, VoIP, email, games, e-commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 8: Network Protocols – Background
How are messages exchanged between hosts in a network?
  exchange of messages follows a well-defined process
  process may be broken-up into several stages
  each stage implements a specific protocol
What is a protocol?
  a set of rules describing the steps, format, and content of messages exchanged between two hosts
  protocol provides a service to an application or another protocol

## Slide 9
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol?

## Slide 10: Protocol “layers”
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing structure of network?
…. or at least our discussion of networks?

## Slide 11: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 12: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 13: Network Protocols – An Analogy
What is the process for flying from Pensacola to Atlanta?
  assume a direct flight, the purchase of an electronic ticket, and bags that must be checked
Baggage (check)
Gates (walk)
Ground (taxi)
Pensacola
Runway (takeoff)
Air (routing)
Air (routing)
Air (routing)
Baggage (claim)
Gates (walk)
Ground (taxi)
Runway (landing)
Air (routing)
Atlanta
departure
arrival
air-traffic control centers

## Slide 14: OSI Reference Model - Background
Open Systems Interconnection (OSI) reference model
  developed by International Organization for Standardization (ISO) in 1970,
  describes networks in 7 layers,
  common framework for developing networking technology and studying networks
  emerged when Internet protocols where in infancy

## Slide 15: OSI Reference Model - Fundamentals
OSI abstracts networks into layers.
Describes important events and steps in network communication.
Layers aids in
  separating different tasks to implement them in either software or hardware
  supporting changes in one or a few layers without impacting other layers
Layers have their own set of protocols and interfaces to communicate with other layers.
Not all layers are implemented in today’s Intranet and Internet

## Slide 16: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 17: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 18: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 19: OSI Reference Model
Session
Transport
Network
Link
Physical
Physical
Physical
Session
Transport
Network
Link
Physical
Application
Presentation
Link
Link
Network
Presentation
Application
Host A
Host B
one or more nodes in network

## Slide 20: Communication Based on OSI Reference Model
Session
Transport
Network
Link
Physical
Application
Presentation
Host A
Session
Transport
Network
Link
Physical
Application
Presentation
Host B
virtual
communication
Data
Data
Segment
Packet
Protocol Data Units
(PDU)
Frame
Data
Bits

## Slide 21: Layer Definitions
OSI Layer | Description
Application | provides access to networking services to user applications PDU is called data
Presentation | handles data representation, conversion, and encryption PDU is called data
Session | sets up and maintains a communication channel between two hosts PDU is called data
Transport | ensures reliability of data transfer data is broken into multiple segments handles sequencing PDU is called segment
Network | handles packet routing, access control in routers as well as logical addressing access control through packet inspection PDU is called packet

## Slide 22: Layer Definitions (cont.)
OSI Layer | Description
Data Link | provides physical device addressing and device-to-device delivery services, provides error detection and correction services implemented in NICs and switches PDU is called frame
Physical | handles bit encoding and decoding into and from binary signals requires networking equipment such as cables, connectors, antennas, …

## Slide 23: PDU of Layers in OSI Model
Data Link Layer Header
Network Layer Header
Transport Layer Header
Data
FCS
Network Layer PDU
Data Link Layer PDU
Transport Layer PDU
Application, Presentation, Session Layer PDU

## Slide 24: Internet Protocol Stack
Uses 5 of the 7 layers from the OSI reference model
Session
Transport
Network
Link
Physical
Application
Presentation
Dropped layers:

## Slide 25: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 26: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
  link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
1
2
two packets,
L bits each
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 27: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 28: Packet-switching: store-and-forward
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 29: Packet Switching: queueing delay, loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 30: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header

## Slide 31: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 32: “Real” Internet delays, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link
* Do some traceroutes from exotic countries at www.traceroute.org
Notes: Choose the server from Princeton University.

## Slide 33: Alternative core: circuit switching
end-end resources allocated to, reserved for “call” between source & dest:
In diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks

## Slide 34: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 35: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 36: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
A
B
propagation
transmission
nodal
processing
queueing
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dnodal = dproc + dqueue + dtrans + dprop

## Slide 37
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
Four sources of packet delay
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
* Check out the Java applet for an interactive animation on trans vs. prop delay
Notes: 37

## Slide 38: Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 39: Caravan analogy (more)
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, 1st car arrives at second booth; three cars still at 1st booth.
toll
booth
toll
booth
ten-car
caravan
100 km
100 km

## Slide 40: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)
* Check out the Java applet for an interactive animation on queuing and loss

## Slide 41: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 42: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 43: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck