## Slide 1: CNT4007C: Theory and Fundamentals of Computer Networks
Network Structures
Content derived from various sources including Tomsho et al., Guide to Networking Essentials,
Kurose and Ross, Computer Networking: A Top-Down Approach

## Slide 2: Overview of Network Topologies
Common Network Topologies in LANs.
Signal Propagation in LANs.
Robustness of Network Topologies.
Network Devices and Media.
Network Structures of the Internet

## Slide 3: Network Topology
Computer networks can have a variety of structures.
The selection of the structure of the network is based on several criteria:
  Cost of infrastructure: how expensive is it to connect the sites.
  Bandwidth/Latency determines how much data can be transported and how long will it take to send messages between sites.
  Reliability determines if a network link fails, how will it affect the exchange of messages between all sites in the network.
Network topologies can be depicted as graphs whose nodes represent sites and edges represent direct communication links.

## Slide 4: Network Topology Examples
A
B
C
D
Ring
D
A
B
C
A
B
C
E
Star
D
E
E
G
F
H
Tree
E
E
G
F
H
Bus

## Slide 5: Network Topologies Examples (cont.)
D
A
B
C
E
Mesh
Given n nodes in network,
then the number of edges in a mesh network is:

## Slide 6: Hybrid Fiber-Coaxial (HFC) Access Network
Cable modem divides HFC network into two channels for uploading and downloading data.
Fiber node
Fiber node
Head node
fiber
cable
fiber
cable
individual homes
coaxial cable
coaxial cable
Neighborhood
Neighborhood

## Slide 7: Signal Propagation in Bus Networks (Ethernet 10Base2)
Sender generates signal and puts it on the wire.
Signal propagates in both directions.
Other hosts listen-in on signal.
Terminator “consumes” the signal.
sending host
terminator
listening host
listening host
listening host
listening host
terminator

## Slide 8: Network Failure in a Bus Network (Ethernet 10Base2)
Signal bounces if in terminators are attached or if network cable is broken.
Bouncing signal generates noise.
no terminator
no terminator
cable broke

## Slide 9: Signal Propagation in Ring Networks (Token Ring)
Sender generates signal and waits for token.
Sender “appends” signal to token.
Signal propagates in physical ring from host to host.
Recipient “consumes” the signal and sends token.
sending host
listening host

## Slide 10: Logical Network Topology - Ring
Physical Topology:
hub connects hosts in a star topology
10 Base-T Ethernet
Logical Topology:
hub receives signal from a host
hub transmits signal in a specific order
order determines logical topology

## Slide 11: A Logical Bus Implemented as a Physical Star

## Slide 12: A Logical Ring Implemented as a Physical Star

## Slide 13: Robustness of Network Topologies
Ring Topology
  less robust because a cable break or a network card failure shuts down the entire network
Bus Topology
  less robust because a cable break shuts down the entire network
Star Topology
  more robust because a cable break only disconnects one host from the network
  failure of hub, switch, router at center of network shuts down the network

## Slide 14: Network Devices
Patch Panel
  serves as junction points between cables coming from switch/hub and wall
  no signal strengthening or filtering
Hubs
  distribute signal across multiple connected ports
  regenerates signal to original signal level (signal strengthening)
  filters any noise
Switches
  Same as hub plus
    determines port of recipient instead of broadcasting the signal to all ports
    reduces overall traffic on network compared to hub by directing the signal

## Slide 15: Network Devices (cont.)
Routers
  strengthen and filter signals
  connect different networks to build larger networks
  routing tables in each router determines the flow of network traffic
  operates at higher level of the OSI model than switches allowing heterogeneous networks to be connected

## Slide 16: Data Transport in Hubs
Hub is a plug-and-play device.
  requires no manual configuration
Frames sent across the network may collide with each other.
No frame buffering.
Hub
segment
host A
host B
host C
host D
When host A sends a frame to host B
no other host may send or a collision
will occur.

## Slide 17: Data Transport in Switches
Switch is a plug-and-play, self-learning device.
  requires no manual configuration
  stores & forwards Ethernet frames using physical address in the frame
  identifies the destination port by observing traffic flow
Switch
segment
host A
host B
host C
host D
Host A and B and host C and D
can exchange messages without
interference.

## Slide 18: Self-Learning Switches
Switch sets up a table to forward frames to destination host.
Switch
segment
host A
host B
host C
host D
1
2
3
4
MAC address | interface | TTL
A | 3 | 60
C | 2 | 60
A | B | ….
Frame
Source
Destination

## Slide 19: Sample Network
Switch
Hub
Hub
Router

## Slide 20: Connecting Hosts to Network
Figure 2-12: Guide to Networking Essentials, 5th Edition, Tomsho et al.

## Slide 21: Combination Star Topology
bus backbone
Figure 2-12 Guide to Networking Essentials, 5th Edition, Tomsho et al.

## Slide 22: Complex Local Area Network
Figure 2-13 Guide to Networking Essentials, 5th Edition, Tomsho et al.

## Slide 23: Complex Local Area Networks (Ethernet)
Small business configured network using
  Ethernet switches
  Routers
  Modem for WAN connection
Ethernet:
  10 Mbs, 100 Mbps, 1 Gbps, 10 Gbps Ethernet
  in a modern configuration, host connects to an Ethernet swith
Router
Switch

## Slide 24: Selecting a Topology
Most new network designs come down to only one choice: How fast should the network be?
The physical topology will certainly be a star, and the logical topology is almost always switching
Ethernet switches are typically used on a LAN, but you might consider other logical topologies for other reasons:
  Use of legacy equipment
  Network size
  Cost restrictions
  Difficulty to run cables

## Slide 25: Creating the Layout
Network must be documented
  Useful questions before drawing the diagram
    How many client computers will be attached?
    How many servers will be attached?
    Will there be a connection to the Internet?
    How will the building’s physical architecture influence decisions, such as whether to use a wired or wireless topology, or both?
    Which topology or topologies will you use?
  Network diagram must be kept up to date
  https://creately.com/

## Slide 26
Creating the Layout (continued)

## Slide 27: Network Structure of the Internet
Internet is a connection of many small networks into larger networks.
Networks may use different network protocols for routing traffic.
  TCP/IP protocol run by almost all personal computers
  Phone companies operate ATM networks.
  Mainframes use SNA network.
Interconnection of networks supports communication between hosts at different locations regardless of network type and protocol.

## Slide 28: Internet Illustration
Home network
Institutional network
Mobile network
Global ISP
Regional ISP

## Slide 29: Connecting Heterogeneous Networks
ATM network
SNA network
FDDI ring
Ethernet
wireless
mainframes
laptop computers using
802.11 to connect to a network
PCs connecting to
an Ethernet
Notes: SNA – IBM – Systems Network Architecture