## Slide 1: CNT4007C: Theory and Fundamentals of Computer Networks
Networking Media / Signal Encoding
Content derived from various sources including Tomsho et al., Guide to Networking Essentials,
Kurose and Ross, Computer Networking: A Top-Down Approach

## Slide 2: Overview of Networking Media
Network Cables in LANs and WANs
  types of networking cables
  characteristics of networking cables
Wireless Networks in LANs and WANs.
Signal Encoding in LANs.

## Slide 3: Media Requirements
Layout of space and devices connecting to network.
Distance and type of cable (wired network):
  How far are connecting networking devices apart?
  How much bandwidth is needed?
  …
Location and number of access points (wireless network):
  How far should the wireless network reach?
  …
Different wired and wireless technology exists but what determines the type of media?

## Slide 4: Cable Characteristics
Bandwidth: capacity for transporting data.
Maximum segment length: length of cable before the signal becomes too weak and distorted.
Maximum number of segments: number of segments between sender and receiver.
Hub/Switch/Router
Hub/Switch/Router
Hub/Switch/Router

## Slide 5: Cable Characteristics (cont.)
Interference susceptibility: interference from outside may generate noise.
Maximum number of devices per segment: each connected device may weaken the signal (bus topology).
Material and installation cost: expensive of cable and its installation.
…

## Slide 6: Primary Cable Types
Cable provide a medium for transporting signals:
Signal type may be light pulses or electrical.
Cable types include
  Coaxial cable
  Twisted pair cable
  Fiber optic cable

## Slide 7: Coaxial Cable
Was predominantly used in early Ethernet.
Has protective shield to protect against interference.
Less susceptible to attenuation than twisted pair.
Higher cost than twisted pair.

## Slide 8: Applications of Coaxial Cables
Early Ethernet for baseband transmission:
  Thicknet (10Base5): strong coaxial cable with up to 500 meters in segment length and 10 Mbps bandwidth.
  Thinnet (10Base2): thinner coaxial cable with up to 185 meters in segment length and 10 Mbps bandwidth.
Broadband transmission of video/audio signal and data to customers.
  enables customers to receive TV signal and Internet data
thicknet
thinnet

## Slide 9: Twisted Pair Cable
Unshielded Twisted-Pair (10BaseT, 100BaseT, 1000BaseT) used widely in LANs.
Shielded Twisted-Pair may be also used in LANs.
  shielding reduces cross-talk and interference
STP
UTP

## Slide 10: UTP Cable Categories
Cables rated based ANSI/TIA/EIA Standard (1991).
  American National Standard Institute
  Telecommunications Industries Association (TIA)
  Electronic Industries Alliance (EIA)
Category | Bandwidth Specifications | Application
Cat. 1 | voice only | telephone cabling
Cat. 2 | up to 4 Mbps | not used any longer
Cat. 3 | up to 10 Mbps (16 MHz) | 10BaseT, 4 Mbps token ring, …
Cat. 4 | up to 16 Mbps (20 MHz) | 10BaseT, 16 Mbps token ring, …
Cat. 5 | up to 100 Mbps (100 MHz) | 100BaseT, ATM, token ring, ..
Cat. 5e | up to 1000 Mbps (100 MHz) | 1000BaseT (Gigabit Ethernet), …
Cat. 6 | up to 1000 Mbps (200 MHz) | 1000BaseT (Gigabit Ethernet), …

## Slide 11: UTP Cable Characteristics
Cat 5, 5e, 6 Characteristics | Description
Maximum cable length | 100 m (328 ft.)
Bandwidth | up to 1000 Mbps
Signaling rates | 100 MHz for Cat. 5 and 5e, 200 MHz for Cat. 6
Material | three twists per inch of each twisted pair of 24 gauge copper wires for Cat. 5 and 5e; more twists per inch for Cat. 6
Connector type | RJ-45 for device and wall-plates
Cost | Least expensive of all cabling options
Security | Moderately susceptible to eavesdropping
Interference rating | low; most susceptible of all electric cable types
Installation | easy to install and maintain

## Slide 12: UTP Cable Connector
Cat5, Cat5e, Cat6 connectors for LAN
Cat1(Telephone line)
RJ-45 (Registered Jack)
RJ-11 (Registered Jack)

## Slide 13: Applications of Coaxial & Twisted-Pair Cable
Coaxial cable from Cable TV provider
UTP patch cable connecting network card with cable modem

## Slide 14: Fiber Optic Cable
inner sheath
kevlar for strengthening cable
optical fiber (glass or plastic)
outer sheath

## Slide 15: Fiber Cable Connectors
Connectors are more expensive than copper wire connectors such as RJ-45 and RJ-11.

## Slide 16: Fiber Cable Characteristics
Characteristic | Description
Maximum cable length | 2 km to 100 km
Bandwidth | 10 Gbps and higher
Material | glass or plastic fiber, plastic sheath, kevlar
Connector type | several types (previous slide)
Cost | most expensive cabling option
Security | not susceptible to eavesdropping
Interference rating | none; least susceptible of all cabling options
Installation | expensive to install and maintain

## Slide 17: Fiber Cable Types
Single-mode:
  higher cost than multimode
  generally works with laser-based emitters,
  spans longer distances than multimode
  bandwidth of up to 50 Gbps for up to 100 km
Multimode:
  less expensive than single-mode
  works with light emitting diodes (LEDs)
  spans shorter distances
  bandwidth of 100 Mbps to 10 Gbps depending on distance (hundreds of meters)
light source
single ray
small
diameter
fiber
light source
multiple rays
larger
diameter
fiber
photodiode
photodiode

## Slide 18: Cabling Summary
Type | Maximum Cable Length | Bandwidth | Installation | Interference | Cost
UTP | 100 m | 10-1000 Mbps | Easy | High | Cheapest
STP | 100 m | 16-1000 Mbps | Moderate | Moderate | Moderate
10Base2 | 185 m | 10 Mbps | Easy | Moderate | Cheap
10Base5 | 500 m | 10 Mbps | Hard | Low | Expensive
Fiber-optic | 2-100 km | 100 Mbps – 40 Gbps | Moderate | None | Most Expensive

## Slide 19: Building Wiring Layout
Equipment room houses
servers and routers.
backbone cabling
to other floors, wings, or
adjacent buildings
wireless access point

## Slide 20: Building Wiring Specifications
Patch cable in work area:
  wiring types include UTP cat. 5 or cat. 5e
  no more than 6 m long between computer and wall jack
Horizontal wiring:
  runs from the office to the telecommunication closet on same floor
  wiring types include four-pair UTP (Category 5e or 6) or two fiber-optic cables
  distance from the wall jack to the patch panel should be no longer than 90 meters

## Slide 21: Building Wiring Specifications (cont.)
Backbone wiring:
  runs between floors or wings of a building and adjacent buildings
  usually fiber-optic cable
  may be UTP for short distances between floors and wings of a building
  distance between equipment room and main cross-connect may be up to 1500 m

## Slide 22: Building Wiring - Examples
server room
telecommunication room
patch panel and switches

## Slide 23
Wireless Networking

## Slide 24: Elements of a wireless network
network
infrastructure
wireless hosts
laptop, desktop, PDA, printer, …
may be stationary (desktop) or mobile (laptop)
Wireless does not always mean mobility.

## Slide 25: Types of Wireless Network
Wireless local area network (WLAN)
  easy to setup and maintain
  provides ad-hoc network access in buildings
  requires wireless network card and access point device
  access point translates radio to electrical signal and vice-versa
Extended wireless LANs
  moderately difficult to setup and maintain
  provides more coverage beyond a typical LAN configuration
  higher equipment cost than WLAN
Mobile computing
  uses cell-phone technology for data transfer
  provides ad-hoc network access anywhere within reach of a radio tower

## Slide 26: Wireless Networking Benefits
Users can create temporary connections to existing wired networks.
Allows easy setup of separate subnet with different security profile.
Provides backup or contingency connectivity for existing wired networks.
Extend a network’s span beyond the reach of wire-based or fiber-optic cabling
  attractive for buildings were wiring would be too expensive or impractical
Enable users to roam with their machines within certain limits (called “mobile networking”)

## Slide 27: Wireless LAN Transmission
Uses electromagnetic waves for data transmission.
Frequency of the wave forms is measured in Hz.
  low frequency waves carry data slower over longer distances than high frequency waves
  low frequency waves emit less energy than high frequency waves
Spectrum of electromagnetic waves for data transmission is divided into three ranges:
  Radio: 10 KHz to 1 GHz
  Microwave: 1 GHz to 500 GHz
  Infrared: 500 GHz to 1 THz

## Slide 28: IEEE 802.11 Wireless LAN (WiFi)
Is an extension of the Ethernet using airwaves.
  Uses same protocol as wired Ethernet
  WiFi hot spot can be directly connected to hub, switch or a router
Includes several standards for wireless data transmission:
Standard | Frequency Range | Data Rate
802.11b | 2.4 – 2.5 GHz | up to 11 Mbps
802.11a | 5.1 – 5.8 GHz | up to 54 Mbps
802.11g | 2.4 – 2.5 GHz | up to 54 Mbps
802.11n | 2.4 – 2.5 GHz | 54 Mbps – 200 Mbps

## Slide 29: IEEE 802.11b/g Wireless LAN (WiFi) Configuration
Access point (AP) must be assigned a channel name and number.
  Each access point is given a MAC address
  85 MHz band (2.4-2.485) can be divided into 11 channels of partially overlapping spectrum of airwaves
  channels separate different APs for better wireless access

## Slide 30: Characteristics of selected wireless link standards
Indoor
10-30m
Outdoor
50-200m
Mid-range
outdoor
200m – 4 Km
Long-range
outdoor
5Km – 20 Km
.056
.384
1
4
5-11
54
IS-95, CDMA, GSM
2G
UMTS/WCDMA, CDMA2000
3G
802.15
802.11b
802.11a,g
UMTS/WCDMA-HSPDA, CDMA2000-1xEVDO
3G cellular
enhanced
802.16 (WiMAX)
802.11a,g point-to-point
200
802.11n
Data rate (Mbps)
data

## Slide 31: Wireless network characteristics
Multiple wireless senders and receivers create additional problems (beyond multiple access):
A
B
C
Hidden terminal problem
B, A hear each other
B, C hear each other
A, C can not hear each other means A, C unaware of their interference at B
A
B
C
A’s signal
strength
space
C’s signal
strength
Signal attenuation:
B, A hear each other
B, C hear each other
A, C can not hear each other interfering at B

## Slide 32: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoded signal = (original data) X (chipping sequence)
decoding: inner-product of encoded signal and chipping sequence

## Slide 33: CDMA encode/decode
slot 1
slot 0
d1 = -1
1
1
1
1
1
-
1
-
1
-
1
-
Zi,m= di.cm
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
channel output Zi,m
sender
code
data
bits
slot 1
slot 0
d1 = -1
d0 = 1
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
1
1
1
1
1
-
1
-
1
-
1
-
slot 0
channel
output
slot 1
channel
output
receiver
code
received
input
Di = S Zi,m.cm
m=1
M
M

## Slide 34: CDMA: two-sender interference
using same code as sender 1, receiver recovers sender 1’s original data from summed channel data!
Sender 1
Sender 2
channel sums together transmissions by sender 1 and 2

## Slide 35: IEEE 802.11 Wireless LAN
802.11b
2.4-5 GHz unlicensed spectrum
up to 11 Mbps
direct sequence spread spectrum (DSSS) in physical layer
  all hosts use same chipping code
802.11a
  5-6 GHz range
  up to 54 Mbps
802.11g
  2.4-5 GHz range
  up to 54 Mbps
802.11n: multiple antennae
  2.4-5 GHz range
  up to 200 Mbps
all use CSMA/CA for multiple access
all have base-station and ad-hoc network versions

## Slide 36: 802.11 LAN architecture
wireless host communicates with base station
  base station = access point (AP)
Basic Service Set (BSS) (aka “cell”) in infrastructure mode contains:
  wireless hosts
  access point (AP): base station
  ad hoc mode: hosts only
BSS 1
BSS 2
Internet
hub, switch
or router

## Slide 37: 802.11: passive/active scanning
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
3
1
passive scanning:
beacon frames sent from APs
association Request frame sent: H1 to selected AP
association Response frame sent from selected AP to H1
AP 2
AP 1
H1
BBS 2
BBS 1
1
2
2
3
4
active scanning:
Probe Request frame broadcast from H1
Probe Response frames sent from APs
Association Request frame sent: H1 to selected AP
Association Response frame sent from selected AP to H1

## Slide 38: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
space
A
B
C
A
B
C
A’s signal
strength
C’s signal
strength

## Slide 39: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK

## Slide 40: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
CTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
avoid data frame collisions completely
using small reservation packets!

## Slide 41: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 42
Signal Encoding in Wired Media

## Slide 43: Types of Signal Transmissions
Broadband transmission
  transmission over a broad spectrum of frequencies
  use analog techniques to encode binary 1s and 0s across a continuous range of values
Baseband transmission
  signals take the form of discrete pulses of electricity or light
  uses a digital encoding scheme (line coding) at a single fixed frequency

## Slide 44: Encoding Schemes in Media (Physical Layer)
What is Encoding?
  Encoding addresses how binary data is converted into these signals.
  Typically implemented in a signaling component (transceiver) that is part of the network interface

## Slide 45: Baseband Transmission
Apply pulse modulation to binary symbol for transmission over digital/baseband channel.
Pulse modulation uses regular sequence of pulses to encode / decode data.
Line coding examples: Alternate Mark Inversion (AMI), Manchester, …
Line Coding Encoder
Digital/Baseband Channel
Line Coding Decoder
1 0 0 1 1
1 0 0 1 1

## Slide 46: Alternative Mark Inversion (AMI)
0 are encoded as 0 volt, 1 is encoded as alternate positive or negative volt.
Problems: long sequence of 0 may cause receiver to become out of sync with sender.
Image from Wikipedia

## Slide 47: Manchester Encoding (line code)
Transmits the exclusive-OR of the clock and signal.
  each bit is transmitted in a fixed time
  a 1 is encoded by a transition from high to low and a 0 by a transition from low to high (G.E. Thomas convention)
Results in a transition every clock cycle.

## Slide 48: Digital Modulation
Uses a sine carrier wave signal to encode data.
  sine carrier wave has low frequency spectrum compared to square waves
Used for transmission over long distances.
Forms of modulation:
  amplitude
  frequency
  phase-shift
Modulation
Analog Channel
Demodulation
1 0 0 1 1
1 0 0 1 1
Carrier