## Slide 1: CNT4007C: Theory and Fundamentals of Computer Networks
Data Link Layer
Content derived from various sources including Tomsho et al., Guide to Networking Essentials,
Kurose and Ross, Computer Networking: A Top-Down Approach

## Slide 2: Overview of Data Link Layer I
Introduction and services
  implementation & adapters
Error detection and correction
Multiple access protocol
Ethernet Frame Structure
Address Resolution Protocol (not quite at Data Link Layer)

## Slide 3: Background on Data Link Layer
Sits on top of the physical layer in the OSI reference model.
Breaks user data from a higher layer into data frames and transmits them sequentially over the physical layer’s communication channel.
Ensures that data are correctly transmitted
  detects transmission errors
  detects loss of data packages
Has built-in traffic regulation mechanisms to let transmitter know when data arrive too fast (flow control).

## Slide 4: Data Link Layer in OSI Reference Model
Virtual data path
Actual data path
Physical Layer
Data Link Layer
Encoding
Framing,
Error detection,
Flow control
Host A
Host B

## Slide 5: Data Encapsulation in OSI Reference Model
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 6: Link Layer Services
Framing and network access
  encapsulating data into frame, adding header and footer
  addressing frame using the MAC address
  accessing communication channel
Reliable deliver between adjacent nodes
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
11000110101000101011
Host A
Host B
LAN
generates a frame
“adjacent” nodes in LAN

## Slide 7: Link Layer Services (cont.)
Flow Control
  adjusting data flow between adjacent nodes in network
Error Detection
  errors may be caused by signal attenuation, noise, etc.
  receiver detects presence of errors in frame
  receiver may request new transmission of erroneous frames
Error Correction
  receiver detects bit error in frame and repairs the frame
Half-duplex, Full-duplex
  two nodes in a ongoing communication may send at same time (full-duplex) or one at a time (half-duplex)

## Slide 8: Where is the link layer implemented?
In each and every host!
link layer implemented in Network Interface Card (NIC)
  Ethernet card, PCMCI card, 802.11 card
  implements link, physical layer
NIC attaches into host’s system buses.
Combination of hardware, software, firmware.
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
host schematic
application
transport
network
link
link
physical

## Slide 9: Adaptors Communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 10
Error Detection Protocol and Reliable Service

## Slide 11: Error Detection / Correction Overview
Errors may occur when transferring data between neighboring nodes in a local network.
Error detection identifies an error but cannot repair it.
  not 100% reliable
Error correction identifies an error and detects it.
  error correction is limited
datagram
frame
EDC’
bit-error prone link between neighboring nodes
frame’
EDC’
all bits
in frame ok?
datagram
y
N
detected error

## Slide 12: Error Detection using CRC (Illustration)
Message (M)
Divide by CRC Polynomial C(x)
Remainder (R)
Concatenate
Transmit over network
Divide by CRC Polynomial C(x)
Remainder = 0 ?
No
Discard Frame
Strip off Remainder
Original Message (M)

## Slide 13: Reliable Transmission in Data Link Layer
Lost or damaged frames must be handled to ensure reliable transmission.
Typically accomplished through retransmissions
  It is possible to encode sufficient information in a frame to actually recover from damaged data (using ECCs - Error Correction Codes)
  However, approaches can only handle limited ranges of errors
  Easier to throw the frame away and transfer the frame again
Relies on two basic mechanisms
  Acknowledgments (ACKs)
    A small control frame that notifies the other end about frames received
  Timeouts
    A mechanism that allows the sender or receiver to wait for a specified amount of time and then take corrective action if the awaited event does not occur.
    Also known as Automatic Repeat Request (ARQ).

## Slide 14: Reliable Transmission – Stop & Wait
Simple scheme
After each frame is transmitted, wait for an ACK from the recipient
If no ACK is received within some timeout period, assume the frame is lost and retransmit
Four possible scenarios:
    ACK is received normally
    Original frame is lost
    ACK is lost
    ACK is received too late

## Slide 15
Media Access Protocol

## Slide 16: Mulitple Access Protocol Overview
Types of links:
  Point-to-Point (PPP)
  broadcast
Point-to-Point
  original dial-up (PPP)
  over Ethernet (PPPoE)
  segment link between host and switch
  router-to-router
Broadcast (shared wired or wireless medium)
  old-fashioned Ethernet
  wireless LAN (803.11, RF)

## Slide 17: Multiple Access Protocol Overview (cont.)
Shared Broadcast Channel:
multiple nodes may access simultaneously channel for transmission
Solution:
  time- or frequency-division multiplexing
  distributed / centralized system that determines when node can transmit
    requires channel for coordination

## Slide 18: Multiple Access Protocol Taxonomy
Over shared media:
Channel partitioning
  divide channel based on time slots, frequency, etc.
  each node is given a designated slot, frequency, etc.
Random Access
  channel may be accessed at any time by node
  may cause collisions that must be addressed
Taking Turns
  nodes take turns to access shared media

## Slide 19: Channel Partition Example
FDM
frequency
time
TDM
frequency
time
4 users
Example:

## Slide 20: Link Layer Protocols: Random Access Protocols
When network nodes have data to send:
  nodes transmit at full channel data rate
  no coordination among nodes on who sends first
When network nodes transmit collision may happen.
  requires technology to detect collisions
  requires protocol to address collisions and recover from them
Random Access MAC Protocol
Examples include:
(slotted) ALOHA
CSMA, CSMA/CD, CSMA/CA

## Slide 21: Slotted ALOHA
all frames are of same size
time is divided into equal size slots
a time slot permits a node to send a frame
nodes are synchronized
nodes start transmitting at slot beginning
if 2 or more nodes transmit in a slot, all nodes detect collision
C
E
S
C
S
E
E
C
E
1
1
1
1
2
2
2
3
3
3
node 1
node 2
node 3
slots
when node obtains fresh frame, it transmits the frame in next slot
  if no collision: node successfully transmitted frame,
  if collision: node must retransmit frame in each subsequent slot with probability p until success

## Slide 22: Carrier Sense Multiple Access/Collision Detection (CSMA/CD)
Used by Ethernets to send frames.
Step 1: Listen on the network before transmitting.
Step 2:
  If no signal detected (channel is idle), transmit frame.
  If signal detected (channel is busy), wait.
Step 3: After frame has been transmitted, check if a collision occurred.
  If no collision detected, frame was successfully transmitted.
  If collision has been detected, wait some time before retransmitting.

## Slide 23: CSMA/CD (Illustration)
sending host
listening host
listening host
listening host
listening host
No Collision!
listening host
sending host
sending host
listening host
listening host
Collision!

## Slide 24: CSMA collisions
collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 25: CSMA/CD (collision detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
human analogy: the polite conversationalist

## Slide 26: CSMA/CD (collision detection)
spatial layout of nodes

## Slide 27: Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:
  after mth collision, NIC chooses K at random from {0,1,2, …, 2m-1}. NIC waits K·512 bit times, returns to Step 2
  longer backoff interval with more collisions

## Slide 28: Taking Turns Access Protocol: Token Passing
Token determines node permitted to transmit.
Token passed from one node to another
sender
recipient
Problems:
  latency for hosts to send data
  single point of failure (if token is lost, it has to be regenerated)
  …

## Slide 29: Taking Turns Access Protocol: Polling
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices.
Problems:
  single point of failure (if primary device fails, no one can send)
  latency for hosts to send data

## Slide 30
Ethernet Frame Structure

## Slide 31: Ethernet
Most widely used LAN network protocol.
  wireless IEEE 802.11
  wired IEEE 802.3
Implementations
  10Base5: Thicknet
  10Base2: Thinnet
  100BaseT, 1000BaseT: Ethernet over UTP
  1000BaseLX, 1000BaseSX: Ethernet over fiber
  10GBaseSR, 10GBaseLR, … : Ethernet over fiber

## Slide 32: Ethernet Architecture
sending host
listening host
listening host
listening host
listening host
Bus Ethernet
Switch
listening host
sending host
listening host
Star Ethernet

## Slide 33: Ethernet Frame Structure
Destination and Source address is 6 bytes long.
  Adapter passes frame into memory if
    destination address matches adapter’s destination address
    destination address is broadcast address
Type in Ethernet Frame indicates higher layer protocol such as IP, Novell, AppleTalk, etc.
CRC checksum is used to detect error in frame, to discard frame.
Preamble
CRC
Dest. Addr.
Source Addr.
Data
Type

## Slide 34: Ethernet Services
Connectionless: sender and receiver do not need to establish a connection prior to sending (hand-shake)
Unreliable: receiver does not sent an acknowledgment to sender.
Media Access:
  CSMA/CD for wired
  CSMA/CA for wireless
Collision Avoidance: The sender must signal intent to
transmit data before it is allowed to access channel and
transmit any data. All other stations may not transmit
until they signal their intent.

## Slide 35
Address Resolution

## Slide 36: LAN addresses and ARP
each adapter on LAN has unique LAN address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 37: LAN addresses (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached

## Slide 38: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 39: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  dest MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 40: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 41: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 42: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 43: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 44: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 45: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy

## Slide 46
Data Transport Devices

## Slide 47: Overview
Repeater
  connects two segments
  regenerates signal to enable data to be transmitted across combined single segment
  operates at physical layer
Hubs
  connects multiple host into a star configuration
  operates at physical layer
Bridge
  connects two LANs
  directs frames between connected LANs to behave like a single LAN
  operates at data link layer

## Slide 48: Data Transport in Hubs
Hub is a plug-and-play device.
  requires no manual configuration
Frames sent across the network may collide with each other.
No frame buffering.
Hub
segment
host A
host B
host C
host D
When host A sends a frame to host B
no other host may send or a collision
will occur.

## Slide 49: Data Transport in Switches
Switch is a plug-and-play, self-learning device.
  requires no manual configuration
  forwards Ethernet frames using physical address in the frame
  identifies the destination port by observing traffic flow
Switch
segment
host A
host B
host C
host D
Host A and B and host C and D
can exchange messages without
interference.

## Slide 50: Ethernet switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 51: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 52: Switch forwarding table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 53: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 54: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 55: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination, A’, locaton unknown:
flood
A’ A
destination A location known:
A’
4
60
selectively send
on just one link

## Slide 56: Interconnecting switches
switches can be connected together
Q: sending from A to G - how does S1 know to forward frame destined to F via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G